## Slide 1: ctDNA-Radiogenomics
14 subjects (3 missing at least one timepoint)
First two timepoints (t1 and t2) subject to analysis
Manual segmentation performed on the series of the highest resolution
Extracted radiomic features within the delineated tumor using PyRadiomics
  https://pyradiomics.readthedocs.io/en/latest/index.html
  First Order Statistics (19 features)
  Shape-based (16 features)
  Gray Level Cooccurence Matrix (GLCM, 23 features)
  Gray Level Run Length Matrix (GLRLM, 16 features)
  Gray Level Size Zone Matrix (GLSZM, 16 features)
  Neigbouring Gray Tone Difference Matrix (NGTDM, 5 features)
  Gray Level Dependence Matrix (GLDM, 14 features)
2-sample t-Test applied to test the group differences at each timepoint.
Timepoint | t1 | t2
Non-Responders | 2 | 2*
Responders | 9 | 8
* Only one subject has both t1 and t2
Notes: Features not normalized prior to extraction.
Parameters:
{'distances': [1], 'additionalInfo': True, 'enableCExtensions': True, 'force2D': False, 'interpolator': 'sitkBSpline', 'resampledPixelSpacing': None, 'label': 1, 'normalizeScale': 1, 'normalize': False, 'force2Ddimension': 0, 'removeOutliers': None, 'minimumROISize': None, 'minimumROIDimensions': 1, 'resegmentRange': None, 'padDistance': 5}

## Slide 2: First-order Features
  Common statistics extracted from the intensity histogram of the image
min intensity
max intensity
mean intensity
standard deviation
90th percentile
10th percentile
Sum intensity
Entropy
skewness
Kurtosis
…more…
Amadasun et al. IEEE Trans Syst Man Cybern 1989, Materka et al. COST B11 Report 1998

## Slide 3: Shape Features
Max Diameters
Compactness
Sphericity
Major/Minor Axis
Elongation
Surface Area
Surface Volume Ratio
Flatness
…more…

## Slide 4: Gray-level Co-occurrence Features
0O
45O
90O
135O
0.17 | 0 | 0 | 0
0 | 0.5 | 0 | 0
0.17 | 0 | 0 | 0
0 | 0.17 | 0 | 0
3x3 image
with 4 possible gray levels
Gray-level co-occurrence
matrix (C) for 0O
Low contrast
High contrast
  Spatial relationship among gray levels in specified directions
0 | 0.33 | 0 | 0
0 | 0.33 | 0 | 0.17
0 | 0.17 | 0 | 0
0 | 0 | 0 | 0
Gray-level co-occurrence
Matrix (C) for 90O
(For simplicity, symmetry is not considered here.)
Haralick et al. IEEE Trans Syst Man Cybern 1973
2 | 0 | 0
1 | 1 | 1
3 | 1 | 1

## Slide 5: Gray-level Run-length Features
2 | 0 | 0
1 | 1 | 1
3 | 1 | 1
0O
45O
90O
135O
Run-length
matrix (R) for 0O
  Texture coarseness in specified directions
Run-length
matrix (R) for 90O
1 | 0
1 | 1
0 | 0
0 | 0
0 | 0
2 | 0
0 | 0
0 | 0
(For simplicity, symmetry is not considered here.)
3x3 image
with 4 possible gray levels
Galloway et al. Comput Graphics Image Process 1975, Chu et al. Pattern Recognit Lett 1990

## Slide 6: Gray-level Size Zone Features
0 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0
2 | 0 | 0
1 | 1 | 1
3 | 1 | 1
  Texture homogeneity in a region
(Rotational invariant)
3x3 image
with 4 possible gray levels
Guillaume Thibault et. al. “Texture Indexes and Gray Level Size Zone Matrix. Application to Cell Nuclei Classification”. Pattern Recognition and Information Processing 2009.

## Slide 7: Neigboring Gray Tone Difference Features
  quantifies the difference between a gray value and the average gray value of its neighbors within distance δ. The sum of absolute differences for gray level i is stored in the matrix.
Amadasun M, King R; Textural features corresponding to textural properties; Systems, Man and Cybernetics, IEEE Transactions 1989.

## Slide 8: Gray Level Dependence Matrix Features
  quantifies gray level dependencies in an image. A gray level dependency is defined as a the number of connected voxels within distance δ that are dependent on the center voxel. A neighboring voxel with gray level j is considered dependent on center voxel with gray level i if |i−j|≤α. In a gray level dependence matrix P(i,j) the (i,j)th element describes the number of times a voxel with gray level i with j dependent voxels in its neighborhood appears in image.
Amadasun M, King R; Textural features corresponding to textural properties; Systems, Man and Cybernetics, IEEE Transactions 1989.
α = 0 and δ = 1

## Slide 9: PyRadiomics
First Order Statistics (19 features)
Shape-based (16 features)
Gray Level Cooccurence Matrix (23 features)
Gray Level Run Length Matrix (16 features)
Gray Level Size Zone Matrix (16 features)
Neigbouring Gray Tone Difference Matrix (5 features)
Gray Level Dependence Matrix (14 features)
http://pyradiomics.readthedocs.io/en/latest/features.html

## Slide 10
Case 83:
Baseline (t1)
RECIST:
Non-responder

## Slide 11
Case 83:
First follow-up (t2)
RECIST:
Non-responder

## Slide 12
Case 43:
Baseline (t1)
RECIST:
Responder
(Stable)

## Slide 13
Case 43:
First follow-up (t2)
RECIST:
Responder
(Stable)

## Slide 14
Case 9:
Baseline (t1)
RECIST:
Responder
(Partial)

## Slide 15
Case 9:
First follow-up (t2)
RECIST:
Responder
(Partial)

## Slide 16
Examples
Of
Normalized
Feature
Vectors

## Slide 17
Shape features

## Slide 18
First order features

## Slide 19
GLCM features

## Slide 20
Runlength features

## Slide 21
Size Zone features

## Slide 22
Gray Level Dependence features

## Slide 23
Neigbouring Gray Tone Difference features
*
*
*
* p < 0.05 between responders and non-responders at t1